## Slide 1: Smart Doorbell
Raspberry Pi + Machine Learning

## Slide 2: The Challenge: Traditional doorbells only alert homeowners of visitors but provide no identification or context about who is at the door.
Current Issues & Our Solution
• No visitor identification >> Real-time face recognition
• Security concerns >> Edge processing (privacy)
• Cloud dependency >> Instant identification

## Slide 3: Primary Goal: Deploying a lightweight ML-based (YuNet+Sface recognition system) on Raspberry Pi that can identify known household members and detect unknown visitors in real-time.
Edge Deployment
Run ML inference directly on Raspberry Pi
Face Recognition
Identify known vs unknown visitors
Real-Time
Instant detection and classification

## Slide 4: System Architecture
Face Capture (capture.py)
Collect and align user faces using webcam → Save as dataset images
Output: Aligned JPG face images per user
Feature Extraction (feature.py)
Convert face images → 128-D numerical embeddings using Sface
Output: User database of embeddings (.npy files)
Real-Time Recognition (recognition.py)
Detect faces → Extract embeddings → Compare → Identify
Output: Real-time identification with name + confidence

## Slide 5: Real-Time Recognition Pipeline
Camera Captures Frame Raspberry Pi camera module captures live video
YuNet Detects Faces Identifies face bounding boxes and landmarks
Face Alignment & Cropping SFace aligns and normalizes detected faces
Feature Extraction Generates 128-D embedding vector
Cosine Similarity Comparison Compares with all stored embeddings in database
Decision: Known vs Unknown If similarity > 0.363 → Recognized (green box + name) If similarity ≤ 0.363 → Unknown (red box)

## Slide 6: Why Yunet
Property | What It Means | YuNet | Compared to Other Detectors (e.g., RetinaFace-ResNet50 / SCRFD-0.5g)
Model Size | Number of learnable parameters → affects memory use + loading speed | 75K parameters → extremely tiny | RetinaFace-ResNet50 ≈ 27M params, SCRFD-0.5g ≈ 631K params → 10×–350× larger
FLOPs | Total operations per inference → determines compute cost | 149M FLOPs @320×320 → very low | RetinaFace-ResNet50 ≈ 11 GFLOPs, SCRFD-10g ≈ 3.3 GFLOPs → YuNet is 20×–70× lighter
Inference Speed (CPU) | Time taken per frame → critical for real-time performance | 2–11 ms depending on resolution | RetinaFace on CPU: 50–230 ms; SCRFD-0.5g: 3–18 ms → YuNet is much faster, especially at higher resolutions
Backbone | Feature extraction network determining accuracy + weight | Custom DWConv-based tiny backbone(12layers) | RetinaFace uses ResNet50 (50+ layers); SCRFD uses heavier CNN blocks → YuNet is far simpler and lighter
Multi-Scale Feature Fusion | How the network handles large vs small faces | TFPN (Tiny Feature Pyramid Network); DWConv-based | RetinaFace FPN uses full convolutions → heavy; YOLO5Face uses PAN → even heavier
Detection Type | Strategy used to predict boxes | Anchor-free, direct regression | RetinaFace, SCRFD, YOLO → anchor-based → require anchor tuning & more post-processing
Small-Face Accuracy | Ability to detect <20 px faces (critical in WIDER FACE Hard) | Strong performance (AP Hard ≈ 0.81) due to emphasis on shallow layers | RetinaFace-R50 ≈ 0.85 AP Hard but much larger and slower; SCRFD-0.5g ≈ 0.68 (smaller version)
Memory Footprint | RAM usage during inference | < 1.5 MB total | RetinaFace-ResNet50 uses 100–200 MB models + activations
Deployment | Usability on edge hardware | Fits easily on Raspberry Pi / IoT / CPU-only devices | RetinaFace/SCRFD often require GPU/optimized CPU kernels for real-time performance
Training Sensitivity | Sensitivity to data scaling, augmentation, distribution | Uses distribution-aware scale augmentation → stable | Large models require massive datasets + careful augmentation to stay stable

## Slide 7: Why SFace
Property | Meaning / Why It Matters | SFace | Compared to RetinaFace (Anchor-based) / UnitBox (Anchor-free)
Scale Handling | Ability to detect tiny → extremely large faces | Hybrid: anchor-based + anchor-free → full-scale coverage | RetinaFace: good small/medium, weak on huge faces; UnitBox: handles huge faces but weaker precision
Architecture Type | How faces are detected | Two-branch system (anchor-based + anchor-free) | RetinaFace: anchor-only; UnitBox: anchor-free only
Backbone Efficiency | Computation needed | Xception-39 → 39M FLOPs (very lightweight) | RetinaFace uses ResNet50 (~7.6 GFLOPs) → ~200× heavier
Bounding Box Regression | Quality of localization | IOU Loss → scale-invariant, robust | RetinaFace uses Smooth L1 → less stable for large-scale variation
Confidence Score Meaning | How reliable the detection score is | Score = predicted IOU → directly tied to box accuracy | RetinaFace score = class probability → not linked to localization
Speed | Real-time capability | ~50 FPS | RetinaFace ~5–8 FPS; UnitBox ~10–15 FPS
Accuracy (WIDER FACE) | Detection performance | Easy 89.1, Medium 87.9, Hard 80.4 | Comparable to RetinaFace; much faster
4K Face Performance | Real-world high-resolution detection | 65.4% AP on 4K-Face | RetinaFace & UnitBox significantly drop on extreme scales

## Slide 8: Hardware and software details
Hardware
Raspberry Pi 4
Main computing unit
Pi Camera Module V2
8MP video capture
Power Supply
5V/3A USB-C adapter
Storage
32GB microSD card
Software
Raspberry Pi OS
Debian-Bookworm
Python 3.8+
Programming language
OpenCV 4.5+
Computer vision library
YuNet + SFace Models
Pre-trained ML models

## Slide 9: Key Features
Real-Time Processing Instant face detection and recognition with 15fps
Edge Computing All processing done locally on Raspberry Pi - no cloud dependency
Privacy Focused Face data never leaves the device - complete privacy protection
Scalable Database Easy to add new users - just capture & extract features
Multi-Face Support Detects and recognizes multiple faces simultaneously
Confidence Scoring Displays similarity score for each recognition

## Slide 10: Challenge’s Faced
Challenge 1: Limited Computing
Raspberry Pi has limited CPU/RAM compared to cloud servers
Solution 1
Used lightweight models (YuNet + SFace) optimized for edge devices. Xception-39 is 200× lighter than traditional models.
Challenge 2: Varying Face Scales
Faces can appear from 10px to 2000px depending on distance
Solution 2
SFace's dual-branch architecture (anchor-based + anchor-free) handles all scales effectively.
Challenge 3: Real-Time Performance
Need to process video frames fast enough for smooth operation
Solution 3
Optimized pipeline with efficient FPN backbone achieves ~20 FPS on edge hardware.
Challenge 4: False Positives
Risk of incorrectly identifying strangers as known users
Solution 4
Carefully tuned similarity threshold (0.363) balances accuracy and false positive rate.

## Slide 11: Results & Demo

## Slide 12: Future Enhancements
Mobile Notifications Push alerts to smartphone when visitor detected (MQTT/Firebase)
Voice Announcements Text-to-speech to announce visitor names via speaker
Delivery Person Detection Train classifier to identify pizza/package delivery uniforms
Event Logging & Database Store timestamps, images, and visitor history in SQLite
Night Vision Support Add IR camera module for low-light/nighttime operation
Two-Way Audio Enable communication between homeowner and visitor
Web Dashboard Remote monitoring interface with live feed and visitor logs
Smart Home Integration Connect with Home Assistant, Google Home, or Alexa

## Slide 13: Thank You!
Any Questions?